## Slide 1: ECG Arrhythmia Detection and Classification
Presenter: Mahdi Khalilzadeh, 9932213
Course: Fundamentals of Intelligent Systems
Lecturer: Dr. Mahdi Aliyari

## Slide 2: TABLE OF CONTENTS 1 4 2 5 3 6
What is ECG?
The Importance of Arrhythmias
Dataset Introduction
Preprocessing
Deployed Models
Results & Further Work
1/14

## Slide 3: What is ECG? 1

## Slide 4: What is ECG?
A bioelectrical signal that records the heart’s electrical activity
Useful for assessing heart rhythm and functionality & detecting heart diseases like arrhythmias
2/14

## Slide 5: The Importance of Arrhythmias 2

## Slide 6: The Importance of Arrhythmias
A condition where the heart beats irregularly, which can lead to serious complications.
Mild or Severe Arrhythmias
Neglection= cardiac arrest = death
3/14

## Slide 7: Dataset Introduction 3

## Slide 8: Dataset Introduction
One of the most widely used and trusted ECG datasets
48 ECG recordings from 47 patients at 360 Hz
Annotated by experts for high accuracy
4/14
Six Considered Classes for this project:
  N (Normal beat)
  A (Atrial Premature Beat)
  V (Premature Ventricular Cont.)
  L (Left Bundle Branch Block)
  R (Right Bundle Branch Block)
  F (Fusion Beat)

## Slide 9: Preprocessing Steps 4

## Slide 10: Preprocessing Steps
5/14
Why? Improve signal quality for better classification accuracy
Noise Removal
Notch filters (30Hz & 60Hz) to eliminate electrical interference & Moving Average
Normalization
Using Z-score normalization to standardize signal amplitudes
Heartbeat Segmentation
Isolating individual heartbeats
Class Balancing
Oversampling and undersampling to prevent bias in the model

## Slide 11: Preprocessing Steps
6/14

## Slide 12: Preprocessing Steps
7/14
[2]
Segmented and Ready!

## Slide 13: Preprocessing Steps
8/20
Sample of Classes

## Slide 14: Deployed Models 5

## Slide 15: Deployed Models
9/14
Logistic Regression
  Simple model serving as a baseline model
  Achieved an accuracy of ~83%
  Performance was limited due to ECG's time-series nature, as logistic regression does not capture temporal dependencies

## Slide 16: Deployed Models
10/14
Long Short-Term Memory (LSTM)
LSTM is a type of Recurrent Neural Network (RNN) designed to handle time-series and sequential data effectively.
Each LSTM cell has three main gates:
Forget Gate: Decides what information to discard.
Input Gate: Determines what new information to store.
Output Gate: Controls what information is passed to the next state.

## Slide 17: Deployed Models
11/20
Why LSTM for ECG?
ECG signals are time-dependent, meaning the previous states of the heart influence the current state.
Accuracy: ~98%
Significantly improved classification of abnormal heartbeats compared to Logistic Regression.
Training is computationally expensive.

## Slide 18: Deployed Models
12/14
Accuracy and Loss

## Slide 19: Conclusion 6

## Slide 20: Conclusion
Machine Learning is effective in automating arrhythmia detection.
LSTMs outperform traditional models due to their capability to capture sequential dependencies.
Models should be tested on other datasets!
13/14

## Slide 21: References
14/14
[1] G. Moody, R. Mark, "The Impact of the MIT-BIH Arrhythmia Database," IEEE Engineering in Medicine and Biology Magazine, vol. 20, no. 3, pp. 45-50, 2001.
[2] B. Ghojogh, A. Ghodsi, "Recurrent Neural Networks and Long Short-Term Memory Networks: Tutorial and Survey," arXiv preprint arXiv:2304.11461, Apr. 2023.

## Slide 22
Do you have any questions?
THANKS

## Slide 23
Model Input:
  ECG signals are received as a sequence of sampled data points.
  Input size: (num_samples, sequence_length, num_features).
LSTM Layers:
  A 64-unit LSTM layer extracts time-dependent patterns from ECG data.
  Return sequences being True ensures outputs are passed forward to deeper layers.
  A final LSTM layer with 32 units learns higher-level temporal dependencies.
Fully Connected (Dense) Layers:
    A Dense layer with 64 neurons processes extracted features.
  A Softmax output layer with 6 neurons calculates the probability for each arrhythmia class.
Model Optimization:
          Loss Function: Categorical Crossentropy for multi-class classification.
        Optimizer: Adam optimizer for accuracy improvement and error reduction.
        Training: The model is trained for 400 epochs, with performance evaluated on validation data at each step.
LSTM Architecture
Bonus!/14